## Slide 2: Assignment + Deliverables
Exploratory Data Analysis
Feature Engineering
Build Model
Hyperparameter Tuning
Model Evaluation
Explainability

## Slide 3: Time allocation – 80/20 rule
Effort spend:
  ~2 days
  Not all steps done (to the needed extend)
Aim:
  Give idea on how I approach
  Questions that came up along the way
"Playing the whole game": A data collection and analysis exercise with Google Calendar - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/The-80-20-rule-of-data-wrangling_fig2_339550606 [accessed 25 Oct 2024]

## Slide 4: Git Repository
https://github.com/JeroenBuil/deegtal_coding_task
For this project
Stack:
  Python
  VSC
Packages:
  MNE
  SKLearn
  Matplotlib
  DIY
In reserve
Stack:
  MS Azure
  Databricks
  SQL
  Power BI
  …

## Slide 5: Exploratory Data Analysis
What are we dealing with?
  Data quality?
  Preprocessing?
  Patterns?e
Quick Stats:
2 Groups
  Unknown conditions
  Unknown stimuli
5 recordings each
  Recording time: ~20-25min
  Fs: 250 Hz
  Filtering: 125 Hz lowpass

## Slide 6: Data Quality - Consistency
Different recording methods (30ch vs 36ch)
Different experimental procedure (photic stim vs ?)

## Slide 7: Data Quality – Ch names
Channels not in 10-20 montage naming
  => Fix + set_montage()
  => Simplifies working with MNE
https://info.tmsi.com/blog/the-10-20-system-for-eeg

## Slide 8: Referenced?
https://pressrelease.brainproducts.com/referencing/

## Slide 9: Re-referencing?
https://www.learningeeg.com/montages-and-technical-components

## Slide 10: Artifacts in EEG Signals and Preprocessing
Non-biological/Environment
Powerline noise, traffic
=> bandpass + bandstop filtering
Biological
eye blinking, movement, respiration, and heartbeat
Often same freq range => grounding, linear regression methods
https://otc-cta.gc.ca/eng/railway_noise_measurement
A Survey on Artifacts Detection Techniques for Electro-Encephalography (EEG) Signals - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/a-EEG-Signals-with-Artifacts-Caused-by-b-ECG-Signals-and-C-EMG-Signals-25_fig3_281887837 [accessed 23 Oct 2024]
https://pmc.ncbi.nlm.nih.gov/articles/PMC861531/
Eye Blink Artifact Detection With Novel Optimized Multi-Dimensional Electroencephalogram Features - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/Frontal-epileptiform-discharges-and-eye-blink-from-CHZU-database_fig1_353475354 [accessed 23 Oct 2024]

## Slide 11: Filtering
Done:
  Bandpass: 0,5-100 Hz
  Notch: 60 Hz
  Crop start + end of recording
Note done (but should be!)
  Remove EOG + ECG artefacts
    => regression / ICA + (NN) Model

## Slide 12: EDA conclusion
Crucial info is missing: Source information + Meta data
  What is separating the groups? => can steer analysis + feature engineering
  Where/how/by whom is recorded?
Consequence:
Unnecessary long puzzling
Risk of false comparison/assumptions between groups
No Source + Metadata == No (usable) Data

## Slide 13: Feature Engineering

## Slide 14: Intermittend Photic Stimulation
Pulse train found in some recordings
  Unfortunately not all channels

## Slide 15: No consistent stim found
Don’t know what is done
If these recordings are comparable
Group | Recording | Channel | Mean
1 | 1 | BURSTS | 0.339228
1 | 2 | BURSTS | 0.0
1 | 3 | BURSTS | 0.0
1 | 4 | BURSTS | 0.392392
2 | 1 | BURSTS | 0.237873
2 | 2 | BURSTS | 0.0
2 | 3 | BURSTS | 0.0
2 | 4 | BURSTS | 0.0
1 | 1 | IBI | 22.108351
1 | 2 | IBI | 0.0
1 | 3 | IBI | 0.0
1 | 4 | IBI | 10.253176
2 | 1 | IBI | 1.674255
2 | 2 | IBI | 0.0
2 | 3 | IBI | 0.0
2 | 4 | IBI | 0.0
1 | 1 | PHOTIC-REF | 0.000003
1 | 2 | PHOTIC-REF | 0.000002
1 | 3 | PHOTIC-REF | 0.0
1 | 4 | PHOTIC-REF | 0.000004
2 | 1 | PHOTIC-REF | 0.000003
2 | 2 | PHOTIC-REF | 0.0
2 | 3 | PHOTIC-REF | 0.0
2 | 4 | PHOTIC-REF | 0.0

## Slide 16: Spectogram (time-freq analysis)
Many windows = many samples!
(not as good as more subjects)

## Slide 17: Where to take window?
Ideally:
  Events that subjects are in same mental state
  Same (lack of) ext. triggers / all in resting
  HOWEVER: No epochs/annotation/description
Assumption: all subjects same mental state + physical state + same procedure
This is clearly not the case, but limited time => cutting corners
10s windows + 5 sec overlap
  Nyquest: 0.5-100 Hz => >= 4 sec window

## Slide 18: Build model + Model Evaluation + Explainability

## Slide 19: ML Models
Unsupervised
  + fast, no pre knowledge, unbiased
  - less info to train
Supervised
  + use class info to your advantage
PCA
tSNE
XGBoost
CNN?
Preferred
Further exploration!?
Clustering

## Slide 20: Unsupervised
I like it: can help give indication of what happens in data
PCA => linear technique

## Slide 21: XGBoost
Gradient boosted decision tree
When in doubt => Use XGBoost!
  + Not sensitive to scaling
  + High performance
  + Easy feature importance tools

## Slide 22: How does it do?
Needs translation to back to freq + bin

## Slide 24: Spectograms = image => NN is the solution
Write down CNN architecture

## Slide 25: Heat Map

## Slide 26: Hyperparameter tuning

## Slide 27: Stuff that affects performance
Filtering
Window length
Nr of windows
Spectogram:
  Resolution
  Freq Range
XGBoost:
  Feature selection
  Depth
  N-times
  CrossValidation
NN:
  Layers
  Nodes
  Training
    Time (epochs)
    Learning rate
  Loss function
  …

## Slide 28: Next steps
More real life solution
CNN => LSTM to enable real time decoding
  => just feed in each window and find long and short term patterns

## Slide 29: Next steps
The main standard about software in medical devices are:
IEC 62304. It deals with the software lifecycle, i.e. almost everything about what software engineers do.
IEC 60601-1 is applicable to embedded software in a hardware medical device,
IEC 82304-1 is applicable to standalone software, also known as Software as a Medical Device (SaMD),
IEC 81001-5-1 adds requirements about cybersecurity,
IEC 62366-1 adds requirements about man-machine interface ergonomics.

## Slide 30: Conclusions

## Slide 31: Conclusions
Data info crucial for design
Design is crucial for data choice
NN lend themselves good for images
Training more challenging
Explainability more challenging => heat map could help identify patterns